CKT-IRSENSE v3.0 User Manual

Operation

The CKT-IRSENSE is an inexpensive infrared proximity sensor, designed primarily for model railroad use. At the top of the device are two small lenses - one emits a series of infrared pulses, which are then reflected by objects into the other lens, a receiver. By measuring the intensity of the returned pulses, the sensor can detect the presence and distance to an object.

Mechanical Installation

The detector is designed to be installed up through the benchwork in a 5/32 inch (4 mm) hole. Be sure that both lenses are clear to shine up between any ties or ballast.

The module is not naturally water resistant, so be careful when ballasting. Some amount of water resistance can be added by coating everything (other than the lenses) with liquid electrical tape or similar sealant. Be very careful not to cloud or cover the detector lenses.

The sensor can be secured in the hole using

Electrical Connections

The CKT-IRSENSE needs 5-18 volts of clean direct current (DC) power to operate. Noisy power supplies may cause issues with detection, and supply voltages exceeding 20VDC may damage the device. The red wire should be connected to the positive side of the power supply and the black lead to the negative.

Two outputs are provided, both of which are “open drain” (otherwise known as “open collector”). This means that they act like a switch to the ground / negative lead. When an output is “active”, it will conduct current to ground. When an output is “inactive”, it will act like an open circuit and not pass current at all. Each output line can handle a maximum of 0.25 amps, and should be exposed to no more than a 40VDC supply.

<FIXME: diagram showing LED connection>

If a logic level output is desired, use a 4.7k-10k ohm resistor to connect the output to the positive supply.

The white output is active when the sensor is detecting an object. The blue output is active when the sensor is not detecting an object.

Changing the Detection Range

The CKT-IRSENSE is pre-calibrated to a typical detection range and needs no user adjustment for most applications.

However, we've left the option to select other detection ranges for special use cases. By

Suggested Uses

- Trigger a sound event using a CKT-SQUEAL sound player
-