CKT-IRSENSE v3 User Manual
# Operation
The CKT-IRSENSE is an inexpensive infrared proximity sensor, designed primarily for model railroad use. At the top of the device are two small lenses - one emits a series of infrared pulses, which are then reflected by objects into the other lens, a receiver. By measuring the intensity of the returned pulses, the sensor can detect the presence and distance to an object.
# Mechanical Installation
The detector is designed to be installed up through the benchwork in a 3/8 inch (10 mm) hole. To install in existing track, first drill a 1/16” pilot hole between the ties. Then, from the bottom, drill a 3/8” hole up toward the track, using the pilot hole you just drilled as a guide. Work slowly and be very careful to not damage the ties (you might want to remove a couple ties first and reinsert them after drilling the hole). Once the sensor is installed, be sure that both lenses are clear to shine up between any ties or ballast.

The module is not naturally water resistant, so be careful when ballasting. Some amount of water resistance can be added by coating everything (other than the lenses) with liquid electrical tape or similar sealant. Be very careful not to cloud or cover the detector lenses.

The sensor can be secured in the hole using a variety of methods such as hot glue or a bracket. See the Iowa Scaled Engineering website for more details and some example mounting methods.
# Electrical Connections
The CKT-IRSENSE needs 5-24 volts of clean direct current (DC) power to operate. Noisy power supplies may cause issues with detection, and supply voltages exceeding 25VDC may damage the device. The red wire should be connected to the positive side of the power supply and the black wire to the negative.

Two outputs are provided, both of which are “open drain” (otherwise known as “open collector”). This means that they act like a switch to the ground / negative lead. When an output is “active”, it will conduct current to ground. When an output is “inactive”, it will act like an open circuit and not pass current at all. Each output line can handle a maximum of 0.25 amps, and should be exposed to no more than a 40VDC supply. The white output is active when the sensor is detecting an object. The blue output is active when the sensor is not detecting an object.

<FIXME: diagram showing LED connection>

If a logic level output is desired, use a 4.7k-10k ohm resistor to connect the output to the positive supply.

# Activation Time
The activation time is factory set to 0.1 seconds. The outputs will indicate that an object has been detected if the object is present over the sensor for 2 consecutive readings spaced 100ms apart. This helps eliminate errant readings. As a consequence of this, though, there will be a slight (0.1s) delay for an object being detected. For most model railroad applications, this is not an issue.

If longer (or shorter) activation times are required, we can provide custom programmed devices. Please contact us with your requirements.
# Release Time
The release time is factory set to 0.1 seconds. The outputs will indicate that an object is no longer detected if the object is not present over the sensor for 2 consecutive readings spaced 100ms apart. This can be used to debounce the detector outputs to stop the outputs from toggling, for example, in the spaces between rolling stock as it travels over the sensor.

Longer release times are available by connecting a resistor between the yellow wire and ground (black wire). The release time can be adjusted up to 20s according to the following table:

R vs. Time Table

R vs. Time graph
# Sensing Distance
The CKT-IRSENSE is pre-calibrated to a typical detection range (~ X inches) and needs no user adjustment for most applications. If other sensing distances are needed, contact us for custom programmed devices. The detection range can be changed from X to Y inches (typically) based on the reflectivity of the object being sensed.
# Applications
- Activate grade crossing signals
- Trigger a sound event using a CKT-SQUEAL sound player
- Block detection
- Occupancy detection on hidden tracks
- End-of-track indication in hidden staging yards